## Slide 1: OMI is Solving the Industry's Need for Bandwidth and Capacity and is now Scaling to DDR5
Pekon Gupta
(SMART Modular Technologies)
Aug 2, 2022

## Slide 2: Phases of Successful OMI Adoption
Applications
Integration
Electrical Connectivity (cables, backplanes)
Mechanical support (Form-factor, CEM/EDSFF)
Thermal requirements
  Development
  Protocol standardization
  Silicon Development
  Multiple suppliers
Enablement
Modifications to BIOS
OS Device drivers
Management plugins
Library / API suport
Hardware
Software
https://openmemoryinterface.org/omi-products/
https://opencapi.github.io/oc-accel-doc/
Notes: Technology Adoption depends on multiple factors, and usually occurs in multiple small steps of enabling eco-system.
*Hardware eco-system*
  Hardware Development. This includes
    Adding support of protocol in Host CPU processor,
    Development of protocol controller silicon which can decode the protocol layers on the device side.
    There should be multiple vendors or supplier of the hardware to foster competiveness and innovation
    OMI and OpenCAPI met this goal by standardization of protocol stack and Differential DIMM form-factor through JEDEC.
    As of today there are multiple suppliers of Differential DIMM modules like SMART Modular, Micron and Samsung using ASIC controller like SMC 1000 series from Microchip as Memory buffer.
  (2) Next step in adoption is integrating the hardware in production quality system. This is where rubber meets the road, and technology gets tested under real workloads and system environment.
  Constrains of Signal Integrity, Thermal and Mechanical compatibility are visible at this stage.
  OpenCAPI and OMI was adopted in IBM’s Power-9 and Power-10 servers as primary interface to connect Memory, thereby cementing the concept into a real working machine.
  (3) Lastly Software eco-system plays a big role in technology adoption.
  Rate of adoption is faster if there is minimal changes required in the software to make use of the technology.
  Adoption becomes seamless, if protocol layer can be encapsulated in standard software API, already integrated with existing software frameworks.
  IBM and other OpenCAPI member companies have contributed numerous lines of software code to opensource repositories, enabling other companies to reuse and benefit from their effort.

## Slide 3: Comparing Memory Interfaces
Attributes | DDR4 (LRDIMM) | DDR5 (LRDIMM) | HBM2E (8 High) | OMI (w/ DDR4 DRAM)[1] | CXL (w/DDR5 DRAM)
Channel Bandwidth (R+W) | 25.6GB/s x (8 Ch) | TBD x (8 Ch) | 400GB/s | 64GB/s x (8 ch) | TBD x (8 Ch)
Latency | 41.5ns | 35-45ns | 60.4ns | 45.5ns | <100n (estimated)
I/O Pin count[2] | Parallel (288 pins) | Parallel (288 pins) | Parallel (1024) | Serial (84 pins) | Serial (84 pins)
Driver Area/Channel | 7.8mm2 | TBD | 11.4mm2 | 2.2mm2 | TBD
Connection | Multi-Drop | Multi-Drop | Point-to-Point | Point-to-Point | Point-to-Point
Data Resilience | Parity | Parity | Parity | CRC | CRC
[1] Sources: (a) White Paper on The Future Of Low-Latency-Memory by Jim Handy and Tom Coughlin of Objective Analysis, (b) https://openmemoryinterface.org/about/
[2] Form-factor dependent
Parallel Interfaces
Serial Interfaces
Notes:   On the left there are parallel interfaces
  ¼ the pins of DDR
  HBM-like bandwidth
  Moves DRAM signaling away from main board onto DDIMM
  Reduces processor’s I/O power
  data throughput rate of 25.6GB/s with a latency of 40ns

## Slide 4: OMI Hardware: Differential DIMM (DDIMM) and E3.S
Sources; The Next Platform Sep. 2021
JEDEC standardized Differential DIMM (DDIMM), available in 1U, 2U and 4U variants.
Standard SFF-TA-1002 connector. Mechanically compatible with NVMe SSDs.
1U DDIMM
2U DDIMM
4U DDIMM
2U DDIMM
4U DDIMM
E3.S (2U)
Moving to DDR5 DRAM
https://www.youtube.com/watch?v=ZDtaanCENbc
  Supports on-board processing (encryption) along with protocol bridging
  1 read and 1 write port per channel, with 8 unidirectional differential lanes.
On board power circuit like DDR5, simplified Host power design
Differential DIMM (DDIMM) form-factor can accommodate up to 512GB Memory
Using DDR4 DRAM

## Slide 5: Platform Integration: Proof of Low-Latency OMI IBM’s Power-10 Server
IBM’s Power-10 E1080 system has multiple DDIMM slots, but “no” DDR4 or DDR5.
  Up to 16TB memory in a single node is enabled using OMI.
  Giving Over 400GB/s bandwidth per socket.
  With Memory Transparent Encryption, and Controller managed ECC/redundancy.
Sources; The Next Platform Sep. 2021
IBM Power E1080 systems with DDR4 DDIMM Slots
Recommended Demo: https://www.ibm.com/demos/it-infrastructure/product.html#15/1985;IBM_Power_Interactive_Update/index.html
https://www.youtube.com/watch?v=ZDtaanCENbc
Search for “IBM Z16 Facility Tour!” on YouTube

## Slide 6: Key Takeaways
  References: https://www.nextplatform.com/2021/09/08/this-is-what-the-most-powerful-server-in-the-world-looks-like/
  https://objective-analysis.com/uploads/2021-04-18%20Objective%20Analysis%20White%20Paper%20%E2%80%93%20The%20Future%20of%20Low-Latency%20Memory.pdf
OMI is a building block for Memory Disaggregation.
  OMI gives HBM2E like bandwidth, DDR4 like latency at ¼ the number of pins than DDR4 DIMM.
  OMI decouples interface between Processor and Memory.
  Works with DDR5, DDR6 and future Persistent or volatile technologies.
  OMI works with existing eco-system of hardware form-factors and software frameworks.

## Slide 7: Trivia
  References: https://www.nextplatform.com/2021/09/08/this-is-what-the-most-powerful-server-in-the-world-looks-like/
  https://objective-analysis.com/uploads/2021-04-18%20Objective%20Analysis%20White%20Paper%20%E2%80%93%20The%20Future%20of%20Low-Latency%20Memory.pdf
Did you know: OMI Transaction and Data Link Layer IP code is available for “Free” without any royalty?
  Yes, OMI Transaction and Data Link code for both Host Controller and Memory Buffer IP can be found at
  https://openmemoryinterface.org/reference-designs-enablement/
  IP also has different code versions optimized for both FPGAs and ASIC implementations.
Did you know: AMD, IBM, SMART Modular and other OpenCAPI members are enabling
  FPGA based (Xilinx) PCIe Development Platform
  Fully functional OMI Transaction and Data link layers, and Traffic generators
  Supports OpenCAPI FMC+ to two OMI DDIMM Sockets Adapter
Did you know: OpenCAPI and OMI have two separate websites ?
OMI (Open Memory Interface) is low latency optimized version of OpenCAPI.
OMI Website: https://openmemoryinterface.org/
OpenCAPI Website: https://opencapi.org/