## Slide 1: A Survey of Form Factors for NVM Express™
Organized & Moderated by: John Geldman
Panel members: John Geldman, Paul Kaler , Michael Lavrentiev, Dave Landsman

## Slide 2: A short panel introduction
John “KIOXIA” Geldman (yours truly): Current Board Member of NVM Express and SNIA, Past Board Member of SD Card Association and CompactFlash Association, PCI-SIG contributor, SNIA SFF TA contributor
Paul “HPE” Kaler: Responsible for researching and evaluating future storage and interconnect technologies and defining the server storage strategy for HPE ProLiant servers, active in SNIA SFF TA, PCI-SIG, OCP NIC and Storage
Bill “Nantero” Gervasi: So many JEDEC roles that we don’t have space
Michael “WDC” Lavrentiev: SD Card contributor, …
Dave “WDC” Landsman: Current Board Member of CompactFlash, NVM Express, SD Card Association, and SNIA, …

## Slide 3: A Survey of Form Factors for NVM Express
NVM Express is now ubiquitous across pretty much ‘all’ storage
Hyperscalars, Enterprise Servers, Desktops, Laptops, Digital Cameras, Cinema Cameras, Drones, Industrial, IOT
Servers & EDSFF get a lot of attention
This panel will share about EDSFF and also, the rest
  (at least what I knew to invite…)

## Slide 4: PCI-SIG Defined Form Factors
John Geldman, KIOXIA

## Slide 5: CEM Add In Card (AIC)
1-16 lanes
Published for PCIe® Base R5.0, under development for PCIe Base 6.0
Every other function option beyond NVM Express…
Size Options:
  Standard Height (111.28 mm) or Low Profile (68.09 mm)
  Length (varies: up to 312 mm, 241.30 mm recommended)
  Single, Dual, or Triple Slot
Strengths:
  The leading edge and workhorse of PCIe FFs
  Backwards compatible to PCIe Rev 1.0
  Supports up to 600 W (Air Cooling stops at 300 W!)
  Supports up 1.5 KG!

## Slide 6: CEM NVMe Examples

## Slide 7: SFF 8639 Connector Module (U.2)
4 lanes
Published for PCIe Base R4.0, under development for PCIe Base R5.0
Size Options: 69.85 mm x 100.45 mm x (5 to 19 mm)
Mostly used for Enterprise and Data Center Storage
Strengths:
  Chassis compatible with SAS and SATA 2.5 inch HDDs
  The go-to enterprise storage since 2012 (the Enterprise SSD Form Factor Forum)
Weaknesses?
  Will PCIe Gen 5 be the most we can pull out of this connector/pinout?
  Can SFF-TA-1001 be supported at Gen 5 or higher speeds?

## Slide 8: U.2 SSD Examples

## Slide 9: M.2 (Mini Express)
2-4 lanes, published for PCIe Base R4.0, under development for PCIe Base R5.0
Size Options: Too Many
  M.2 Cards (typically 22 mm wide for SSDs, lengths include 30, 42, 80, 110 mm)
  Two families of BGA pinouts starting at 11.5x13 mm and 16x20 mm
  LGA options
Developed for mobile, but consumed in:
  Hyperscalars, Enterprise Servers, Desktops, Laptops, Digital Cameras, Cinema Cameras, Drones, Industrial, IOT
Strengths:
  Low power at acceptable performance (e.g., 11 W, 8 W, 4 W)
  Wide range of functions available
  Wide range of sizes
Weaknesses?
  Will Gen 5 be the most we can pull out of this connector/pinout?

## Slide 10: M.2 (Mini Express) Examples
Adapter Cards
BGAs
LGAs

## Slide 11: SNIA SFF TA Defined Form Factors (and SNIA Object TWG)
Paul Kaler, HPE

## Slide 12: EDSFF
(Enterprise and Datacenter Standard Form Factor)
E3 Family
E3.L 2T
E3.L
E3.S 2T
E3.S
E1.S
5.9mm
8.01mm
9.5mm
15mm
25mm
9.5mm
18mm
E1.L

## Slide 13: E3 Family
Supports up to x4/x8/x16 lane width spec’d up to PCIe Gen5
  Future plans for Gen6 and beyond
E3.S and E3.L support 7.5/16.8 “2T” (mm) thicknesses
7.5mm targets mainstream capacities and performance
2T (16.8mm) is for higher capacity (e.g. 60TB) and/or full Gen5 performance (>25W)
Current defined protocols– NVM Express, CXL, Native NVMe-oF
  Future OCP NIC 3.0 enablement
Predominately used in Enterprise servers and storage
  Future—use E3.S anywhere a 2.5” drive is used today
Strengths: Works well for both 1U and 2U servers, 2 for 1 interchange (2x 1T↔2T), scalable thermals—full Gen5 and beyond performance, x16 lane width enables performance headroom

## Slide 14: E1.S
Supports up to x4/x8 lane width spec’d up to PCIe Gen5
  Future plans for Gen6 and beyond
Five thickness options 5.9/8.01/9.5/15/25 (mm)
Current defined protocols– NVM Express, CXL, Native NVMe-oF
Predominately used by Hyperscalers
Strengths: Optimized for 1U servers, wide range of thickness options provide ability to tailor for varying thermal, density, and performance requirements

## Slide 15: E1.L
Supports up to x4/x8 lane width spec’d up to PCIe Gen5
Two thickness options 9.5/18 (mm)
Current defined protocols– NVM Express, CXL, Native NVMe-oF
Predominately used by Hyperscalers for “cooler” storage tiers (e.g. QLC)
Strengths: Very optimized to achieve high capacity (~1PB) in 1U servers and JBOFs

## Slide 16: SFF-TA-1001 (U.3)
Supports up to x4 lane width spec’d up to PCIe Gen4
Based on PCI Express SFF-8639 Module Spec Rev 4.0 with a new pinout that enable tri-mode host drive bays
PCIe lanes are shared with SAS/SATA enabling tri-mode RAID controllers to support NVMe/SAS/SATA with one to four ports
Predominately used in Enterprise servers and storage
Strengths: Sharing high speed lanes enables lower cost systems for mixing SAS/SATA/NVMe and makes it easier for customers to transition from SATA/SAS to NVMe

## Slide 17: Native NVMe-oF Drive
Supports up to x2 lane width spec’d up to Ethernet 25G
  Future plans under development for Ethernet 50G
Spec supports several form factor options (2.5”, 3.5”,and EDSFF)
Predominately targeting use cases where performance scaling per drive is important
Strengths: Enables end-to-end Ethernet connectivity eliminating potential performance bottlenecks with Ethernet to PCIe conversions.

## Slide 18: JEDEC Defined Form Factors
Bill Gervasi, Nantero

## Slide 19: XFM (JESD233)
1-2 lanes, published for PCIe Base R4.0
Card Size
  14 mm wide, 18 mm long, 1.4 mm thin
Developed as replaceable storage (not removable)
Strengths:
  Embedded connectorized storage
  A balance between a small form factor and support of SSD-class components (e.g., current and future 3D flash)
  2.5 V and 1.2 V power inputs
  Four current classes for targeted performance and power

## Slide 20: XFM
Embedded connectorized storage designed for:
  Easy replacement
  Minimal real-estate (3D)
  Heat transfer mechanisms optimizable for system target

## Slide 21: Automotive BGA
JESD312

## Slide 22
Variety of Control Systems
PCIe
Switch
Communications
SoC
Display
SoC
Vehicle Control
SoC
Entertainment
SoC
PCIe Shared Resource:
Automotive
SSD

## Slide 23
Target: Year End 2022
A New Standard SSD
for automotive applications

## Slide 24
Sufficient power delivery
Case exposed for cooling
PCI-SIG 2828 BGA
28 mm
28 mm
1.2 – 2.0 mm
0.8 x 0.8 mm pitch
Package & Pinout
Ref: PCI Express M.2 Specification

## Slide 25
16x20
20x24
22x28
To assist suppliers in offering well priced options without sacrificing compatibility:
End users design to 2828, allow any part to drop in
Allows suppliers to use any of the footprint compatible options
  16 x 20 mm
  20 x 24 mm
  22 x 28 mm
  28 x 28 mm
28x28

## Slide 26
PCIe 4.0 x4
32 GB/s peak throughput
Automotive
SSD
JTAG
SMBus
Electrical Interface
Ref: PCI Express Base Specification 4.0

## Slide 27
Command Protocol
Ref: NVM Express (NVMe) protocol
Required:
PCIe 4.0
Encouraged:
Single Root I/O Virtualization
Ref: PCI Express Base Specification 4.0
Required:
NVMe 1.4c+
Physical interface
Logical interface
System and power management
Testability
Required:
SMBus
Ref: System Management Bus (SMBus) Specification
Required:
JTAG
Ref: JTAG (IEEE 1149.1) Specification
Optional virtualization

## Slide 28
Security
Ref: Security Protocol and Data Model (SPDM)
Ref: Digital Signature Standard (DSS)
Ref: FIPS PUB 180-4 Secure Hash Standard (SHS)
384-bit Minimum Security
Ref: NIST Platform Firmware Resiliency Guidelines 800-193
Ref: Component Measurement and Authentication (CMA)
Signature: TPM_ALG_ECDSA_ECC_NIST_P384
Hash: TPM_ALG_SHA_384
SPDM
Truth Boundary
Secure
Request
Secure
Response
Firmware
Resilience
Responder
Requester

## Slide 29
Storage Regions
Drive Capacity Class | Minimum System Region Capacity | Bulk Region Capacity
128 GB | 0 | 128 GB
256 GB | 0 | 256 GB
512 GB | 32 GB | 512 GB
1 TB | 32 GB | 1 TB
2 TB | 64 GB | 2 TB
4 TB | 64 GB | 4 TB
Optional Feature:
High reliability system storage region
Bulk Storage
Boot code
Operating System
Critical Apps
E.g.,
SLC
E.g.,
MLC
The system and bulk regions may have distinct parameters including temperature range, retention, etc.
E.g., Terabyte Write (TBW) for -40C to +95C supported for system and storage regions, -40C to +105C for system region only

## Slide 30
Endurance
Ref: JESD218B-01 Solid State Drive (SSD) Requirements and Endurance Test Method
Ref: JESD219 Solid-State Drive (SSD) Endurance Workloads
Personal Auto
344 days/year
3 hours/day
15 year life
Professional Auto
365 days/year
12 hours/day
8 year life
Defined by
Market Segments
Professional Auto market, bulk storage region capacity 1 TB class from -40 to +95 C = 200 TBW
DWPD = 200 TBW [ 1 TB * 8 years * 365 days/year * (12 ÷ 24 hours) ] = minimum 0.24 DWPD
Personal Auto market, system storage region capacity 64 GB from +95 to +105 C = 12.8 TBW
DWPD = 12.8 TBW [ 0.064 TB * 15 years * 344 days/year * (3 ÷ 24 hours) ] = minimum 0.31 DWPD
Data usage model = Enterprise model
TBW = Terabytes written
DWPD = Drive writes per day

## Slide 31: SD Card Defined Form Factors
Michael Lavrentiev, WDC

## Slide 32: SD Express Card - Basics
The fastest SDTM and microSDTM memory cards with backward compatibility
Supporting the following interfaces:
  NVMeTM + PCIe ® interface – up to PCIe 4.0 x2
  SD interface (UHS-I up to 105MB/s)
PCIe
G3x1
PCIe G3x1
PCIe G3x2
PCIe G4x2
PCIe G4x1
3938B/s
1969MB/s
985MB/s
104MB/s
/7.1)
SD and related marks and logos are trademarks of SD-3C LLC. © 2022 SD-3C LLC. All Rights Reserved.
32.0×24.0×2.1 mm
15.0×11.0×1.0 mm

## Slide 33: SD Express Card – Features
Initiate either directly from the PCIe/NVMe or SD
  Fully compatible to PCIe/NVMe standards. Identifies itself as a standard NVMe Memory
ESD protection up to 4KV on all pads (Same as legacy SD card requirements)
Hot Plug-In/Removal support
Boot, TCG and RPMB (SD9) may be supported by the SD interface as well
Working on New Speed Classes over NVMe (1)
(1) Forward-looking statement: SDA undertakes no obligation to realize these forward-looking statements, which speak only as of the date hereof.
SD and related marks and logos are trademarks of SD-3C LLC. © 2022 SD-3C LLC. All Rights Reserved.

## Slide 34: SD Express - Applications
VR & AR video
increasing in quality  requires a high-speed real-time view of 360o
Gaming with 3D high-resolution graphics  requires more memory and high-speed capability for real-time usage
Multi Channel Video Capturing  requires multi-stream high speed recording and captures large amount of data
4K cameras are everywhere
Plus growing 8K, 12K and 8k360o VR cameras with huge data/speed requirements
(8K/24fps uncompressed requires 6GB per minute or 360GB per hour!)
Off-the-shelf bridge solutions allow full support of SD-UHS-II cards as well as SD Express enabling smooth transition
  Multi-sensor Data Collection
  And/or
  Multimedia Apps running from cards
  Semi-embedded applications (IoT, Mobile-Compute etc)
SD and related marks and logos are trademarks of SD-3C LLC. © 2022 SD-3C LLC. All Rights Reserved.
Notes: We see a never-ending growing need for memory capacity and performance…
[Read the title.. And bullets]
Relating the ‘off-the-shelf’ bridge – that is proposed by Bayhub… though hosts may design it also by them self's. The connectors allows it.

## Slide 35: CompactFlash Defined Form Factors
Dave Landsman, WDC

## Slide 36: CompactFlash Association
Charter
Create a standards-based removable storage ecosystem for the professional/prosumer imaging, automotive/industrial markets.
History
Established 1995 by SanDisk and a group of Consumer Electronics manufacturers during infancy of digital photography to establish the CompactFlash into an industry standard
Standards evolved through CFA’s successful 27-year history from PCMCIA to PCIe®+NVMe®. Widely adopted by professional and prosumer digital cameras and camcorders
Membership
81 Corporate Members consisting of Host, Card, Peripheral and Tester manufactures
Americas = 25, Japan = 25, Asia = 20, Europe = 11
Addressable Markets
Professional Imaging
Renowned professional photo and video camera manufacturers have been loyal to CompactFlash since its inception for its performance, capacity, and reliability
Automotive and Industrial
Data acquisition, analysis, and storage is key to AI-based industrial and autonomous transportation applications

## Slide 37
CFexpress
Value Proposition
Highest performance, highest capacity, and highest reliability removable storage solution for the market
Notes: CF Express announced
CF Express 1.0 had only Type B, derived from XQD for Gen3 only
CF Express 2.0
Added Type A and C
Still 1 lane (8GT/s)
Type B is most widely adopted today; Type A is being adopted
On type A: Sony out, other coming
Cards: Three vendors have product (Delkin, Sony, Prograde)
CFA adopting NVMe/PCIe
Is CFA declining. No.
One nice thing of CF is larger capacity due to larger form factor

## Slide 38: CFexpress: Why NVMe®/PCIe®?
 | NVMe | PCIe
Solid foundation | Optimized for low latency NVM Exploits platform parallelism Efficient SW stack | No HBA P2P transfers
By ~2015, NVMe & PCIe had added various features applicable to mobile and removable cards | Host memory buffer (less/no DRAM in device) Enhanced Power Management Boot, Write Protect, RPMB | L1.2 Sub-states (low power)
Continued development | Data placement interfaces, driven by datacenter which optimize latency/QoS (ZNS, FDP, …) | FW Attestation Link encryption
Other advantages across NVMe/PCIe ecosystem | Hot plug infrastructure Better integration w/ internal storage | 
      Why NVMe/PCIe?
      Datacenter to Removable; Investment and Innovation

## Slide 39: Full BIO Slides

## Slide 40: John Geldman Director, SSD Industry Standards at KIOXIA
Member Board of Directors, NVM Express
Member Board of Directors, SNIA
Co-Chair NVMe-MI
Currently an active contributor to the following standards organizations:
    NVM Express, INCITS T10, INCITS T13, JEDEC, PCI-SIG, SATA IO, SNIA, IEEE SISWG
    In addition, John’s team members are also active in CXL, DMTF, TCG, OCP
Corporate leadership responsibility for standards for multi-billion dollar storage vendors since 2011
Involved in storage standards since 1992, with an early introduction to standards including the transition from X3T9 to ATA & SCSI, and the transition from PCMCIA to CardBus
An active FMS CAB member for at least 10 years

## Slide 41: Paul Kaler Future Storage Architect at HPE
Brings over 20 years of experience to his current role where he is responsible for researching and evaluating future storage and interconnect technologies and defining the server storage strategy for ProLiant servers
Actively involved in multiple standards and industry organizations, and has been a key driver of standards including U.3, EDSFF E3, and the OCP Datacenter NVMe SSD spec.
Previously led development of SSD storage arrays, been founder and co-founder of a couple of startups, and helped develop the first dual-screen smartphone.

## Slide 42: Bill Gervasi, Principal Systems Architect, Nantero, Inc.
Mr. Gervasi has over 40 years of experience in high speed memory subsystem definition, design, and product development. Career highlights include 19 years at Intel where he was systems hardware designer, software designer, and strategic accounts manager. Mr. Gervasi subsequently was with S3 where he was a graphics architecture specialist and at Transmeta as memory technology analyst. Most recently he held several key positions with companies such as Netlist, SimpleTech, and US Modular driving unique memory module configurations. He is now Principal Systems Architect for Nantero, developing non-volatile RAM-class memories.
Mr. Gervasi been involved in the definition of Double Data Rate SDRAM since its earliest inception. He has served on the JEDEC Board of Directors and chaired committees for DRAM parametrics and small form factor memory modules during the development of DDR1 through DDR5. He is currently the chairman of the JEDEC Alternative Memory committee.

## Slide 43: Michael Lavrentiev Technologist, Systems Engineering at Western Digital
Chair of SWG at SDA since 2018
Developing SD Express since Nov 2016
Contributor to SDA since 2012
Contributed for the development of new generations of market leading SD and microSD cards.
Handled product management and product requirements for various flash memory solutions.
Before joining Western Digital, worked at KLA-Tencor, RSIP, Gyrus-ACMI and Intel.
Earned M.Sc. in Electrical Engineering from the Technion – Israel Institute of Technology.

## Slide 44: Dave Landsman Sr. Director, Distinguished Engineer, Western Digital
Manages storage standards across Western Digital’s businesses.
Active in storage standards since 2008, representing SanDisk and then Western Digital.
Contributions to NVMe, PCI-SIG, JEDEC, SATA-IO, T10, T13, SNIA, SFF, and others.
Currently WD’s board representative for NVMe, SNIA, CFA and DNA Data Storage Alliance.
Has stopped counting years in the industry. Had “first career” at Intel, “second career” in storage at msystems/SanDisk/WD, and a startup in between.
BA in computer science from the University of California, San Diego. Aside from UCSD Pascal, most coding in ancient asm (VAX/PDP-11/misc).